## Slide 1: IHE Devices – SDPi Supplement
SDC is a registered trademark of OR.NET
Introduction & Overview
<date> 2020
(Version 1.2 2020.10.30A)

## Slide 2: IHE Germany – SDC / SDPi Plug-a-Thon – Briefing
IHE Basics - Why profile?
From ISO/IEEE 11073 SDC to IHE SDPi TF to PATs & CATs
Orientation Tour: IHE Technical Framework & SDPi Profiles
IHE SDPi TF-3 SDC/BICEPS Content Modules & Specializations
IHE SDPi TF-2 Transactions & MDPWS Messaging
IHE SDPi Profile Option Specifications

## Slide 3: First … Term Usage & Assumptions
SDC Service-oriented Device Connectivity Family of ISO/IEEE 11073 SDC standards Assumption: PAT participants have a working understanding of SDC
SDPi Service-oriented Device Point-of-care Interoperability Set of (4) IHE technical framework profiles based on ISO/IEEE 11073 SDC standards Assumption: PAT participants may have some working knowledge of IHE & TF profiles
PAT Plug-a-thon IHE testing event intended for early, informal exploration of new tech & new profiles Assumption: PAT participants may have background in “hackathons”, plugfests, etc.
CAT Connectathon IHE formal interoperability testing event for published profiles; includes independent monitors, test management tooling; published results Assumption: PAT participants may have background in formal test invents

## Slide 4: Second … Profiles? Why?!
Isn’t a well architected family of standards sufficient?
The needs of an implementation community are often both narrower than the set of possible applications that are covered by foundational / core standards, such as ISO/IEEE 11073 SDC, as well as broader in scope requiring additional standards to be integrated.
Why profiles?
As users and implementers agree how to use standards to address specific integration needs, optionality must be minimized, coordinated usage of multiple standards considered, and national / regional allowances factored
IHE Profile A technical specification that constrains a set of general open standards for application to a specific interoperability or integration need (described by a set of use cases) 1
1 Not to be confused with an HL7 FHIR Profile, which is similar in concept but very different in application

## Slide 5: IHE Process Overview
Source: https://www.ihe.net/about_ihe/ihe_process/

## Slide 6: IHE Plug-a-thon (PAT) Basics
IHE Testing Events –
Pathway to CA & Certification!

## Slide 7: <Add a simple CAT overview slide / graphic>
SDC / SDPi Distinctives … SOA / DPI / PnT / SOMDA …WS*
Drives CA & Tooling challenges!

## Slide 8: Orientation Tour: IHE TF & SDPi Profiles
https://www.ihe.net/uploadedFiles/Documents/PCD/IHE_PCD_WP_SDPi_Rev1-1_Pub_2019-11-01.pdf
https://wiki.ihe.net/index.php/SDC@IHE_White_Paper
2019 SDPi paper established rationale and strategy for profiling ISO/IEEE 11073 SDC in IHE Technical Framework profile specifications.

## Slide 9: <from Use Cases/Scenarios to Profiles to Test Scripts>
Profiles constrained to test scripts (full circle – see IHE Process overview)
Link to detail in SDPi profiles / supplement (from narrative to Gherkin)
Drives profile requirement => test plan / test cases / scripts …

## Slide 10: Orientation Tour: IHE TF & SDPi Profiles
Source: https://www.ihe.net/uploadedFiles/Documents/Templates/IHE_TF_General_Introduction.pdf

## Slide 11: Orientation Tour: Example – IHE DEC Profile
TF-1 Profile calls out TF-2 Transaction(s) – may add usage constraints
NOTE: Only message profiling specifications included, relying on references to base message standards for all additional details.
TF-2 Common Transaction Message Elements are Specified Once in Appendices

## Slide 12: Orientation Tour: Example – IHE DEC Profile
TF-3 Bindings only generally referenced in DEC profile & DEV-01 Transaction
General semantic content profiling specifications
Device Specializations – Apply General to Specific types

## Slide 13: Orientation Tour: IHE TF & SDPi Profiles
Service-oriented Device Point-of-care Interoperability (SDPi)
Four profile specifications:
  SDPi-P for Plug-and-Trust Interoperability
  SDPi-R for Reporting Medical Information
  SDPi-A for Alerting
  SDPi-xC for External Controlling
Three IHE DEV TF Volumes:
  TF-1 Profiles / use cases / actors / …
  TF-2 Transactions / MDPWS messaging
  TF-3 BICEPS content modules / device specializations
See draft SDPi Supplement Word Document for additional content detail & outline (https://github.com/IHE/sdpi-fhir/tree/master/SDPi%20%20Supplement/SDPi%20Rev%201.0)

## Slide 14: Orientation Tour: From Volume 1 to 2 to 3
SDPi TF Supplement Vol.1 Integration Profiles
  SDPi-P Profile
    Profile Actors & Transactions & Content Modules
    Profile Actor Options
    Profile Overview (Concepts & Use Cases)
    SES Considerations
  SDPi-Reporting Profile …
  SDPi-Alerting Profile …
  SDPi-xControl Profile …
  Appendix A: Requirements Management for Plug-n-Trust Interoperability
  Appendix B: ISO/IEEE 11073 SDC Requirements Coverage
    <including ISO/IEEE 11073 SDC ICS tables>
  Appendix C: Device Point-of-care Interoperability Use Cases
  <including Gherkin detail & links to Compendium etc.>
SDPi TF Supplement Vol.2 Transactions
  DEV-23 Announce Network Presence
  Scope
  Actor Roles & Referenced Standards
  Messages (at BICEPS level w/ links to Appendix A)
  Protocol Requirements
  SES Considerations
  DEV-24 Discover Network Participants
  …
  DEV-44 Invoke Medical Control Services
  Appendix A: ISO/IEEE 11073 SDC / MDPWS Message Specifications (Normative)
  SDC/BICEPS to SDC/MDPWS Message Specifications
  Messages for BICEPS Discovery Model
    <specific MDPWS message links>
    <example exchanges & library calls>
See SDPi Supplement (1.0) document in the IHE sdpi-fhir Github repository for full details.
M:N Profiles & Transactions
MDPWS Message Detail in Appendix

## Slide 15: Orientation Tour: From Volume 1 to 2 to 3
SDPi TF Supplement Vol.1 Integration Profiles
  SDPi-P Profile
    Profile Actors & Transactions & Content Modules
    Profile Actor Options
    Profile Overview (Concepts & Use Cases)
    SES Considerations
  SDPi-Reporting Profile …
SDPi TF Supplement Vol.2 Transactions
  DEV-23 Announce Network Presence
  Scope
  Actor Roles & Referenced Standards
  Messages (at BICEPS level w/ links to Appendix A)
  Protocol Requirements
  SES Considerations
  DEV-24 Discover Network Participants
  …
See SDPi Supplement (1.0) document in the IHE sdpi-fhir Github repository for full details.
SDPi TF Supplement Vol.3 Content Modules
  DEV Semantic Content Modules
  General Device Content Considerations
  …
  SDC / BICEPS Semantic Content
  DEV Specialization Content Modules
  Device: Infusion Pump
  …
  SDC / BICEPS Content Module
  Device: Ventilator …
  Device: Physiologic Monitor …
  Devices: Surgery … (new)
  Devices: Anesthesia … (new)
  Devices: Dialysis … (new)
Bindings – General & Specific

## Slide 16: Orientation Tour: From 11073 SDC to SDPi
Initially, map to TF-3 DEV Content Modules / Device Specializations
Can include content before specializations published
Eventually, may inform IHE DEV Device-Specific Profiles
Pre-publication, will reference in SDPi SES sections (TF-1, -2 & -3)
Post-publication, can fully integrate requirements into SDPi (incl. TF-1 Appendix B conformance)
NOTE: (4) profiles are aligned with these (4) key purposes
SDC/BICEPS (-10207) Referenced in all (3) volumes (TF-1, -2 & -3)
SDC/SOMDA (-20701) Referenced in TF-1 & TF-2
SDC/MDPWS (-20702) Referenced primarily in TF-2 (esp. Apdx. A)

## Slide 17: <add SES in SDPi TF slide here>

## Slide 18: Orientation Tour: IHE Profile Actor Diagrams
SDPi-P Actor Diagram
SDPi-A Actor Diagram
IHE Actor
  “information systems or components of information systems that produce, manage, or act on health information”
IHE Abstract Actor
  Specifies behavior that is shared across / inherited by a set of IHE Actors (actor name in italics & dotted line around concrete actors)
Profile “External” Actor
  Indicates actors that are outside the scope of the profile but interact with profile actors (dotted box) Note: actor may be defined in other profiles
IHE Grouped Actor
  Indicates actors that integrate with other actors to provide their functionality (two rectangles joined side-by-side)

## Slide 19: Orientation Tour: SDPi-P (Plug-and-Trust)
SDPi-P Actor Model
NOTE: SOMDS Participant actors may be devices, system applications, SAMD, “smart apps” …

## Slide 20: Orientation Tour: SDPi-P (Plug-and-Trust)
SDPi-P Actor Model
SDPi-P Options (partial)
Current Proposed Options
See SDPI Profile Option Specifications section for detail on each

## Slide 21: Orientation Tour: SDPi-P (Plug-and-Trust)
SDPi-P Actor Model
SDPi-P Transactions
See SDPI Transaction Specifications section for detail on each

## Slide 22: Orientation Tour: SDPi-P (Plug-and-Trust)
Example of an SDPi-P transaction exchange …
For a full set of profile-specific MDPWS sequence exchanges, see:
  https://confluence.hl7.org/display/GP/SDPi+Technical+Framework+Models
NOTE: Definition of “BICEPS” abstraction level for SDPi transactions.

## Slide 23: Orientation Tour: SDPi-P (Plug-and-Trust)
Example of an SDPi-P transaction MDPWS sequence
For a full set of profile-specific MDPWS sequence exchanges, see:
  https://confluence.hl7.org/display/GP/SDPi+Technical+Framework+Models

## Slide 24: Orientation Tour: SDPi-R (Reporting)
SDPi-R Actor Model
NOTE: Transactions are drawn to the dotted box around the gateways, indicating that they can be either Provider and / or Consumer SDPi-R actors
See SDPI Transaction Specifications section for detail on each

## Slide 25: Orientation Tour: SDPi-A (Alerting)
SDPi-A Actor Model
See SDPI Transaction Specifications section for detail on each

## Slide 26: Orientation Tour: SDPi-xC (External Control)
SDPi-xC Actor Model
See SDPI Transaction Specifications section for detail on each

## Slide 27: SDPi-P Option Specifications

## Slide 28: SDPi-P Options: Streaming
Define related:
  transactions,
  MDPWS sequences,
  SOMDA Constraints,
  Content Module Bindings
  SDPi 1.0 or subsequent?
  …
Transactions are the same as for SDPi-R -> only transport layer is different!
Out of scope for SDPi 1.0 – securing the waveform channel is extra-challenging; adds unnessecary complexity with questionable performance benefit
2020.11.04
  Secured waveforms in 1.0 (default) … MDPWS out-of-the-box;
  Consider unsecured UDP streaming for 1.x (upon request only)
  OR as an alternative transport HTTP/2 gRPC in 1.x
  ADD UML version of THIS SDPi-R & add to Appendix A Waveform Service section

## Slide 29: SDPi-P Options: Safe Data Transmission
Define related:
  transactions,
  MDPWS sequences,
  SOMDA Constraints,
  Content Module Bindings
  SDPi 1.0 or subsequent?
  …
Transactions are the same except for the message payload
Out of scope for SDPi 1.0 unless a party claims need – safe data transmission is conceptually fuzzy and brittle. Would require very specific profiling
2020.11.04
  Message Payload is the only difference … & relies on XML;
  @ gRPC – is fundamentally different & challenges (e.g., not using xpath)
  Wait for -10703 for specific value proposition (incremental over baseline) +
  May use this or alternative to current MDPWS (ambiguity)

## Slide 30: SDPi-P Options: Compact Representation
Define related:
  transactions,
  MDPWS sequences,
  SOMDA Constraints,
  Content Module Bindings
  SDPi 1.0 or subsequent?
  …
Transactions are the same except for the message serialization
There are no serious EXI implementations on the market; SDPi should recommend/require use of HTTP compression; which is not optimal but widely adopted
2020.11.04
  EXI is a “beast” of a spec; SDC libraries do not support – little market support either
  HTTP/2 + gRPC would address out of the box
  HTTP/1.1 … good enough , but …gzip for example FOR SDPi 1.0 for every transaction w/ option; in every transaction section
  NOTE: Sequence of serialization & compression of message content varies per approach
  NOTE: A key application need is for performance at scale – e.g., streaming 100’s of beds with 12 lead per bed
  Consider whole SOMDS running in “compressed” mode
  Add note to MDPWS Appendix A + as TBD @ EXI use; call out the HTTP/1.1 approach

## Slide 31: SDPi-P Options: Patient Context Management
Define related:
  transactions,
  MDPWS sequences,
  SOMDA Constraints,
  Content Module Bindings
  SDPi 1.0 or subsequent?
  …
I guess I need more context here (hihi). Let‘s talk about that on Wednesday
2020.11.04
  Defer (?) to SDPi 1.x – what is needed NOW vs. when connecting to enterprise applications
  MUST do something in 1.0 to ensure safety of all exchanges – IOW what is IN this option vs. must be supported by the base SDPi-x profiles? In SDPi-P vs. –R / -A / -xC require it
  What use cases NOW will rely on this? A Patient-Device Association Management Source of Truth within a System of Products / SOMDS implementation
  What will be baked into the related PKP standards? – the preconditions are baked into the PKP, not how you can make sure the data is the needed Quality (e.g., reliability)

## Slide 32: SDPi-P Options: Archive Service
Define related:
  transactions,
  MDPWS sequences,
  SOMDA Constraints,
  Content Module Bindings
  SDPi 1.0 or subsequent?
  …
I can prepare best-practice sequences; nevertheless the Archive Service as specified in BICEPS does not cover all variations of archival access – backfilling yes, full closure no
2020.11.04
  No real experience / use case that drives the message exchanges …
  Therefore, no way to VALIDATE that what is supported is sufficient
  Supports 5-10 minutes / off-line period for “backfilling” … network connection loss only – no Provider restart etc.
  Not 100+ hours of full disclosure … this would require a different persistence layer & …
  Relationship with (MDIRA/ICE) DataLogger Actor specification?
  SDPi 1.0 will be narrow Provider off-line backfilling & SDPi 1.x / MDIRA for Full-Disclosure of a forensics data logging capability TBD

## Slide 33: SDPi-P Options: Localization Service
Define related:
  transactions,
  MDPWS sequences,
  SOMDA Constraints,
  Content Module Bindings
  SDPi 1.0 or subsequent?
  …
I can prepare best-practice sequences by inspecting our productive implementation
2020.11.04
  Change option name to Language Service
  Use in SDPi 1.0
  NOTE: different from LocationContext support
  Example message content is the interesting part!

## Slide 34: SDPi-P Options: Ensemble Participation
Define related:
  transactions,
  MDPWS sequences,
  SOMDA Constraints,
  Content Module Bindings
  SDPi 1.0 or subsequent?
  …
This is a hard nut to crack – we‘ll have general rules in PKP, but the magic happens beyond that ruleset.
We don‘t have any experiences right now, just some learnings from Dräger‘s CAP leveraging the location context… much room for development here
2020.11.04
  Need to establish INITIAL base use cases for SDPi 1.0 …
  This is closely related to the SFC definition / management
  Identify basic use of SystemContext objects for this use
  Basic “fixed” workplace … establish base sequence / approach w/ constraints
  NOTE: SES & clinical workflow / personnel “understanding” is key
  TBD use of mobile devices or multi-patient (spot check) devices, etc.
  Related to Patient-Device Association (Patient Context) Option
  Advanced could factor in:
    Mobile devices
    Patient centric devices (e.g., blood gas measurement or telemetry)
    CLC actors
    …

## Slide 35: SDPi TF-2 Transactions & MDPWS Messaging

## Slide 36: SDPi TF-2: DEV-23

## Slide 37: SDPi TF-2: DEV-24

## Slide 38: SDPi TF-2: DEV-25
Both opts are unnecessary if the BICEPS interface is known a-priori – which it is partially  we might need some additional profiling to unambigiously determing BICEPS service actions. I‘ll double-check that
Only highly dynamic implementations would require to resolve hosted services and WSDLs – unlikely for medical devices
2020.11.04
  For SDPi: Normatively reference WSDL file from <XYZ> (e.g., IHE Github IO?) ADD to repo etc.
  Make WSDL file mandatory for all SDPi Providers
  ACTION: David G. will update WSDL to remove optionality & ambiguity – cleaner & nicer 
  Include note & future option (???) for retrieving WSDL for each service IF Provider & services are new.

## Slide 39: SDPi TF-2: DEV-26

## Slide 40: SDPi TF-2: DEV-27

## Slide 41: SDPi TF-2: DEV-28

## Slide 42: SDPi TF-2: DEV-29

## Slide 43: SDPi TF-2: DEV-30

## Slide 44: SDPi TF-2: DEV-31

## Slide 45: SDPi TF-2: DEV-32
The loop is based on try-and-error – one could request „nested intervals“ (is that the right term, I only know the German one… and the translators suck sometimes.
The whole ArchiveService – as already mentioned – is wonky and insufficient. Hard to profile, but partially better with HTTP/2
2020.11.04
  Sync with the earlier Option slide context & constraints
  Descriptors will have time frame (e.g., 4 hours) …
  States may be overrun by high frequency data
  Strategy: Approximation by try/fail/try again @ ½ size
  Challenge is staying under the 4MB limit …
  No support now for a “stream” of archive data – only request / response and need to approximate in REAL TIME optimal data frame size.
  NOTE: At HTTP/2 provides simple stream for bi-directional exchange
  Archive 2.0 service may address / or alternative transport etc.

## Slide 46: SDPi TF-2: DEV-33

## Slide 47: SDPi TF-2: DEV-34

## Slide 48: SDPi TF-2: DEV-35
3.35 Establish Medical Data Exchange [DEV-35]

## Slide 49: SDPi TF-2: DEV-36
3.36 Publish Medical Data [DEV-36]

## Slide 50: SDPi TF-2: DEV-37
3.37 Retrieve Medical Data [DEV-37]
Note this is a polled retrieve vs. pub/sub eventing

## Slide 51: SDPi TF-2: DEV-38
3.38 Establish Medical Alert Exchange [DEV-38]

## Slide 52: SDPi TF-2: DEV-39
3.39 Publish Medical Alert Update [DEV-39]

## Slide 53: SDPi TF-2: DEV-40
3.40 Retrieve Medical Alert Status [DEV-40]

## Slide 54: SDPi TF-2: DEV-41
3.41 Manage Medical Alert Delegation [DEV-41]

## Slide 55: SDPi TF-2: DEV-42
3.42 Delegate Medical Alert [DEV-42]

## Slide 56: SDPi TF-2: DEV-43
3.43 Update Alert Acknowledgement Status [DEV-43]

## Slide 57: SDPi TF-2: DEV-44
3.44 Manage Medical External Control [DEV-44]

## Slide 58: SDPi TF-2: DEV-45
3.45 Invoke Medical Control Services [DEV-45]

## Slide 59: SDPi TF-3 SDC/BICEPS Content Modules & Specializations

## Slide 60: SDPi TF-3: SDC/BICEPS Content Modules - General
Topics to be covered in the General BICEPS semantic profiling section:
  Link to TF-1 SDPi-P Content Modules & same for other profiles?
  Extension model
  General (all device specializations)
  SDPi 1.0 or subsequent?
  … (see subsections in outline)

## Slide 61: SDPi TF-3: SDC/BICEPS – Infusion Pumps
Topics to be covered in the BICEPS infusion pump profile section

## Slide 62: SDPi TF-3: SDC/BICEPS – Physiologic Monitor
Topics to be covered in the BICEPS physiologic monitor profile section

## Slide 63: SDPi TF-3: SDC/BICEPS – Ventilator
Topics to be covered in the BICEPS ventilator profile section

## Slide 64: SDPi TF-3: SDC/BICEPS – Surgery Devices
Topics to be covered in the BICEPS surgery devices profile section

## Slide 65
Additional
Information

## Slide 66: Real-world Narrative: Isolation ICU
Pandemic Patients in an Isolation ICU – EUA Remote Control Narrative
In dealing with severely infectious patients, healthcare workers (HCWs) are at a significantly greater risk of infection than the overall population due to their frequency and time in contact with the infected patients. The HCWs will enter the patient room to administer care to the patient and manage the therapeutic equipment. This management of the patient’s therapy may require frequent device adjustments which may be delayed due to the need for the HCWs to protect themselves by donning PPE prior to entering the patient room and doffing the PPE upon leaving. This donning and doffing processes can exceed 15 minutes depending on the specific PPEs used. A recent study (Suen, 2018) reported times of 7 minutes for donning and 10 minutes for doffing, with the doffing process providing the opportunity for “considerable” self-contamination.
Infectious diseases confer a synergistic burden on and risk to the patient due to the requirements for isolating the patient (Abad et al., 2010) including poorer care and impaired coordination of care, (Mehrotra et al., 2013), significantly fewer HCW and family visits (relative to patients not on precautions) (Morgan et al., 2013), increased rate of adverse events (Stelfox et al., 2003) and increased depression (compared to other inpatients). (Day et al., 2011). The use of remote control and monitoring can be used to eliminate some treatment delays, reduce the infection risk to the HCW, and help preserve the limited supplies of PPE and improve patient care.
Critically ill patients with an infectious disease will often require monitoring with physiologic monitors and therapeutic support with ventilators and infusion pumps. As previously explained, entering the room to view parameters or adjust any settings can require 15 minutes for something that may take less than 1 minute. Medical devices that support open interoperability technology can provide remote access to view parameters and adjust settings thereby increasing efficiency, saving the costs of the PPE and most importantly increasing the safety of the HCW.
Source: Adapted from AAMI CR Proposal: “Emergency Use Guidance for Remote Control of Medical Devices"

## Slide 67: Real-world Narrative: Isolation ICU
Pandemic Patients in an Isolation ICU – Scenarios?
For the purposes of this PAT, what scenarios are of greatest interest?
  Participant Discovery / Security / Service Exchange?
  Patient / Participant Association (Patient & Location & Workflow context establishment)?
  Alert delegation / Alert Limit Adjustment / Alert confirmation / Silence ... ?
  Which devices, systems, applications? Monitors, vents, pumps, central … others?
  Integration with EHR or other system?
  Use of IHE-based FHIR profiles for integration with non-SDPi / non-SDC SOMDS systems?
  …
Other Use Cases / Scenarios? (e.g., surgery focused)

## Slide 68: Hanging Gardens: After SDPi 1.0 …
MDIRA ICE Profile
Surgery PoC Profile
NOTE: Profile Titles are notional – hopefully useful too!
ICU PoC Profile
IHE (Official) Profile Types:
  Transport, Content, Workflow
  Or a combination of all (3)
Other types?
  Architecture (SOA, MDIRA, SDC, ….?
  Single domain / multi-domain?
Device Specialization Profile
SOMDS@home Profile
Devices-In-Care (PDP) Profile